## Slide 1
Design an autonomous robot for indoor navigation using A* search for path planning while avoiding obstacles. Equipped with sensors, it dynamically updates its environment knowledge, ensuring real-time path adjustments.
By
Md Sadikur Rahman Sadeed 2112251042
Md.Esak Ali 1921789042
Ahanaf Tahomid 1831920642
Md. Iftekhar Mahmood 2013525042

## Slide 2
Node Class Overview
Essential Element
The Node class is a fundamental part of the A* path planning algorithm. It represents a position within the environment and stores information related to the path planning process.
Key Features
Each Node object holds its position coordinates, the cost of reaching it, and the cost to reach the goal from it. This data enables the efficient calculation of optimal paths.

## Slide 3
Node Class Structure
Position (x, y): Coordinates of the node within the environment.
Parent Node: Reference to the node from which this node was reached.
Path Cost (g): The cost of reaching this node from the starting position.
Heuristic Cost (h): Estimated cost of reaching the goal from this node.

## Slide 4
Node Class Features
Position Tracking: Maintains the (x, y) coordinates of the node within the grid representing the environment.
Parent-Child Relationships: Stores a reference to the parent node, allowing for path reconstruction from goal to start.
Cost Calculations: Calculates the path cost (g) and heuristic cost (h) to guide the search algorithm.
Priority Queue Compatibility: Implements the necessary methods to be used with a priority queue, enabling efficient node sorting for A* search.

## Slide 5
Robot Class Overview
Robot Functionality
The Robot class encapsulates the functionalities of a mobile robot, including its physical characteristics, movement capabilities, and interaction with the environment.
Key Features
This class implements unicycle model kinematics, enabling the robot to move and rotate based on its wheel velocities. It also handles path planning and obstacle avoidance, ensuring safe navigation.

## Slide 6
Robot Parameters
1
Position
(x, y)
2
Orientation
(θ)
3
Wheel Radius
r
4
Base Width
L
5
Sensor Range
d

## Slide 7
Core Functionalities
1
Motion Control
Implementation of control algorithms to move the robot along a desired path, ensuring accurate trajectory following and obstacle avoidance.
2
Path Planning
Utilizing the A* search algorithm, planning a collision-free path from the current robot position to the target location.
3
Obstacle Detection
Utilizing sensors to detect obstacles in the environment, dynamically updating the map to avoid collisions during navigation.
4
State Visualization
Providing a real-time visual representation of the robot's state, including its position, path, obstacles, and map information.

## Slide 8
Motion Control
Sensor data: Sensors provide information about the robot's position, orientation, and surrounding environment.
Control Algorithm: Calculates the desired wheel velocities based on the desired path and current state, ensuring accurate robot movement.
Actuators: Receive control signals from the algorithm and drive the robot's wheels to execute the desired motion.

## Slide 9
Path Planning
A* Algorithm: A* search efficiently finds the shortest path from the robot's current position to the goal while taking into account obstacles.
Dynamic Replanning: The A* algorithm dynamically replanns the path in real-time, adapting to changes in the environment or new obstacle detections.
Obstacle Avoidance: The planned path ensures that the robot avoids collisions with detected obstacles, maintaining safety during navigation.
Goal Tracking: The algorithm continuously tracks the robot's progress towards the goal, adjusting the path as necessary to reach the target.

## Slide 10
Visualization